Liquid Crystal Displays  (LCD)

LCD Module Pin Assignment

| Pin number | Symbol | Level | I/O | Function |
| --- | --- | --- | --- | --- |
| 1 | Vss | - | - | Power supply (GND) |
| 2 | Vcc | - | - | Power supply (+5V) |
| 3 | Vee | - | - | Contrast adjust |
| 4 | RS | 0/1 | I | 0 = Instruction input 1 = Data input |
| 5 | R/W | 0/1 | I | 0 = Write to LCD module 1 = Read from LCD module |
| 6 | E | 1, 1-->0 | I | Enable signal |
| 7 | DB0 | 0/1 | I/O | Data bus line 0 (LSB) |
| 8 | DB1 | 0/1 | I/O | Data bus line 1 |
| 9 | DB2 | 0/1 | I/O | Data bus line 2 |
| 10 | DB3 | 0/1 | I/O | Data bus line 3 |
| 11 | DB4 | 0/1 | I/O | Data bus line 4 |
| 12 | DB5 | 0/1 | I/O | Data bus line 5 |
| 13 | DB6 | 0/1 | I/O | Data bus line 6 |
| 14 | DB7 | 0/1 | I/O | Data bus line 7 (MSB) |

LCD Driver Block Diagram

References : http://www.hantronix.com  Select resources tab and tutorials entry

DISPLAY CHARACTER POSITION AND CHARACTER ADDRESS

Interfacing a 16x2 character LCD to the Infineon 167

Port connections to LCD module - LCD module to be used in 4-bit mode

Port 7			LCD pin

Bit 7			DB7

Bit 6			DB6

Bit 5			DB5

Bit 4			DB4

Port 6

Bit 7			E - Enable

Bit 6			R/W – Read/notWrite

Bit 5			RS – Register Select

‘C’ Functions Required

lcd_initialise 		- initialise lcd for 4-bit mode, 2-lines, etc

lcd_write_data 	- write a byte to be displayed

lcd_write_control	- write a command to the lcd

lcd_read_status	- read the status of the lcd

lcd_read_data		- read the data at the cursor position - ??? do we need this?

lcd_putchar		- “print” a character on the lcd at the current cursor position.

lcd_clear		- clear lcd display

lcd_busy 		- returns 1 if lcd busy, 0 otherwise

lcd_gotoxy		- move lcd cursor to x,y position

lcd_write_nibble	- write a 4-bit nibble to the lcd

maybe lcd_read_nibble

might need to have some delays so maybe a delay function – how accurate should the delays be?

Any others?

It might be good if we could somehow make the standard ‘C’ function print be able to “print” directly to the lcd.

It would be useful to make these functions into an lcd function library.

Which of these should be made available to a user? How can we prevent a user from accessing functions that we don’t want them to access?

Where should we start? We design top down. Implement and test bottom up particularly when we are doing something for the first time or that maybe difficult.

LCD DRIVER (HD44780) instruction set

| Instruction | Code | Description | Execution Time |
| --- | --- | --- | --- |
|  | RS | R/W | DB7 | DB6 | DB5 | DB4 | DB3 | DB2 | DB1 | DB0 |  |  |
| Clear display | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | Clears display and returns cursor to the home position (address 0). | 1.64mS |
| Cursor home | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | * | Returns cursor to home position (address 0). Also returns display being shifted to the original position. DDRAM contents remains unchanged. | 1.64mS |
| Entry mode set | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | I/D | S | Sets cursor move direction (I/D), specifies to shift the display (S). These operations are performed during data read/write. | 40uS |
| Display On/Off control | 0 | 0 | 0 | 0 | 0 | 0 | 1 | D | C | B | Sets On/Off of all display (D), cursor On/Off (C) and blink of cursor position character (B). | 40uS |
| Cursor/display shift | 0 | 0 | 0 | 0 | 0 | 1 | S/C | R/L | * | * | Sets cursor-move or display-shift (S/C), shift direction (R/L). DDRAM contents remains unchanged. | 40uS |
| Function set | 0 | 0 | 0 | 0 | 1 | DL | N | F | * | * | Sets interface data length (DL), number of display line (N) and character font(F). | 40uS |
| Set CGRAM address | 0 | 0 | 0 | 1 | CGRAM address | Sets the CGRAM address. CGRAM data is sent and received after this setting. | 40uS |
| Set DDRAM address | 0 | 0 | 1 | DDRAM address | Sets the DDRAM address. DDRAM data is sent and received after this setting. | 40uS |
| Read busy-flag and address counter | 0 | 1 | BF | CGRAM / DDRAM address | Reads Busy-flag (BF) indicating internal operation is being performed and reads CGRAM or DDRAM address counter contents (depending on previous instruction). | 0uS |
| Write to CGRAM or DDRAM | 1 | 0 | write data | Writes data to CGRAM or DDRAM. | 40uS |
| Read from CGRAM or DDRAM | 1 | 1 | read data | Reads data from CGRAM or DDRAM. | 40uS |

# Text boxes

| Bit name | Settings |
| --- | --- |
| I/D | 0 = Decrement cursor position | 1 = Increment cursor position |
| S | 0 = No display shift | 1 = Display shift |
| D | 0 = Display off | 1 = Display on |
| C | 0 = Cursor off | 1 = Cursor on |
| B | 0 = Cursor blink off | 1 = Cursor blink on |
| S/C | 0 = Move cursor | 1 = Shift display |

| Bit name | Settings |
| --- | --- |
| R/L | 0 = Shift left | 1 = Shift right |
| DL | 0 = 4-bit interface | 1 = 8-bit interface |
| N | 0 = 1/8 or 1/11 Duty (1 line) | 1 = 1/16 Duty (2 lines) |
| F | 0 = 5x7 dots | 1 = 5x10 dots |
| BF | 0 = Can accept instruction | 1 = Internal operation in progress |

Timing Characteristics

READ TIMING

WRITE TIMING

4-Bit Initialisation