State Machines

(See also Finite State Machine, Algorithmic State Machine, State Charts, State Diagram - all related and similar to each other)

Event-driven State Machine - Easy to implement in software

A system can be identified as having several states that it can be in, with input events or input conditions which cause the system to change state (this is called a transition) and in doing so generate outputs. This is the basic state machine idea.

State diagrams are a way of depicting a state machine.

States are drawn as circles, boxes or boxes with rounded corners. The transitions are drawn as arcs between states and are labelled with the input event or condition that causes the transition along with the output generated (input condition / output). An initial starting state is indicated in some way e.g a transition with no starting state

Example: A simple car interior light controlled by a door switch

Implementing State machines in software.

Again there are several ways in which state machines can be realised in software.  One simple method is to use a switch - case structure and a state variable:-

Initialise system variables, inputs and outputs.

state = 0

loop

switch(state)

case 0:

//state 0 code:-

[code to be executed while in this state]

if event1 then

generate output

change state

endif

if event2 then

generate output

change state

endif

break out of switch statement

case 1:

//state 1 code

[code to be executed while in this state]

if event3 then

generate output

change state

endif

if event4 then

generate output

change state

endif

break out of switch statement

etc.

endswitch

goback to loop

The state variable determines which case is executed in the switch statement.. The loop keeps the machine operating.

For the simple interior light

set light bit to output and turn off

set door switch as input

state = 0

loop

switch(state)

case 0:

//state 0 code:-

if door switch open then

light on

state = 1

endif

break out of switch statement

case 1:

//state 1 code

if door switch closed then

light off

state = 0

endif

break out of switch statement

endswitch

goback to loop

For the more complex interior light

set light bit to output and turn off light

set door switch as input

initialise timer hardware

state = 0

loop

switch(state)

case 0:

//state 0 code:-

if door switch open then

light on

state = 1

endif

break out of switch statement

case 1:

//state 1 code

if door switch closed then

start timer

state = 2

endif

break out of switch statement

case 2:

//state 2 code

if door switch open then

stop timer

state = 1

endif

if time period over then

light off

stop timer

state = 0

endif

break out of switch statement

endswitch

goback to loop

# Text boxes

Idle

Lighting

door open / light on

door closed / light off

door open / light on

door closed / Start timer period

door open / stop timer

time period end / light off

idle

light

light for period

An improved version

0

1

0

2

1